## Slide 1: Image Analysis BMB 547 Jonathan Brewer

## Slide 2: Why Image Analysis
As scientists acquire images to get DATA
Image
Regionalize and Measure
Data

## Slide 3: Spatial transcriptomics smFISH
Stochastic Optical Reconstruction Microscopy (STORM): resolution 20-40 nm: N/TERT-1 cells with CK14

## Slide 4
Spatial transcriptomics
Single cell selection and change plotting mode
Notes: It is also possible to select single cells, which updates the plot.
This allows the user to change the plotting mode, where the fold change in gene expression is also available.
Although this visualizer is a robust tool for data exploration, it should be improved further to handle large data sets better.

## Slide 5: Topics:
Basic properties of digital images (sampling, formats, size, depth, )
Image enhancement (how to make your image look better)
  histograms, LUT, contrast enhancement
  background subtraction
  filter masks (smoothing and sharpening)
Working with image stacks
Colocalization
Image segmentation by thresholding
Deconvolution

## Slide 6: Quantitative Imaging? …what does that mean?
Numerical Results
Statistics!
Computers become useful...
Art or Science?
Science means to measure something!

## Slide 7: Which is brighter A or B?
Still sure you can interpret intensities in greyscale images with your eyes?

## Slide 8: Which colours can you see???

## Slide 9: “Colour Merge” images could ruin your life
Actually,
the green and blue...
are the same color!
You see spirals, of pink, orange, green and blue?
Moral of the story:
Don’t Trust Your Eyes!

## Slide 10: What is Image Analysis / Quantification?
255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 50 | 50 | 50 | 50 | 255 | 255
255 | 255 | 255 | 50 | 50 | 50 | 50 | 50 | 255 | 255
255 | 255 | 255 | 50 | 50 | 50 | 50 | 50 | 255 | 255
255 | 255 | 255 | 72 | 50 | 50 | 50 | 50 | 255 | 255
255 | 255 | 255 | 255 | 50 | 50 | 50 | 255 | 255 | 255
255 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 50 | 255
255 | 255 | 255 | 255 | 255 | 50 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 50 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 255 | 50 | 50 | 50 | 50 | 51 | 168
255 | 255 | 255 | 255 | 50 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 50 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 255 | 50 | 255 | 255 | 255 | 255 | 255 | 255
255 | 255 | 50 | 255 | 255 | 255 | 255 | 255 | 255 | 255
Object: Body: Head: Legs: Arms:
Stick man 1
1
2 (1 lifted)
2 (2 lifted)
Walking left to right…
Minimum: 50
Maximum : 255
Mean: 94.5
Std.Dev.: 93.2 Area: 10x14
Pixels: 140
Pix <255: 42
= Image Analysis/ Measurement
= Interpretation of Analysis Result

## Slide 11: Image = Information
Images contain information!!!
Quantify / Measure / Analyse
Meta data (what, where, when, how)
Noise / Background

## Slide 12: Photographer or Spectroscopist?
Is simply a way to “Visualise”
 | 0 | 0 | 1 | 0 | 0
 | 0 | 1 | 0 | 1 | 0
 | 0 | 0 | 1 | 0 | 0
 | 0 | 0 | 1 | 0 | 0
 | 1 | 1 | 1 | 1 | 1
 |  |  | 1 | 0 | 0
 |  |  | 0 | 1 | 0
 |  |  | 0 | 0 | 1
 | 0 | 0
 | 0 | 1
 | 1 | 0
 | x | 
y
This
This

## Slide 13: What is a (Digital) Image anyway..?
A digital image of ???
Image Analysis (Brain or Computer)
A stick man? How do I know?
How can computer know
- algorithm?
• • • • •
• • • • •
• • • • •
• • • • •
• • • • •
• • • • •
• • • • •
• • • • •
=
it’s a digital “representation” of reality!
it’s an artifact that contains less info than the object!
it’s just numbers! NOT analogue art!
The Image of a point is NOT a point!!! (Point Spread Function – PSF)
x
y

## Slide 14: The digital image: pixel size
Photons induce transport of electrons.
Transport of electrons generates voltage.
Generated voltage is proportional to number of incoming photons.

## Slide 15: The point spread function (PSF)
The point spread function (PSF) describes the response of a microscope to a point source or point object.

## Slide 16: Pixel Size / Image Resolution
1 Airy unit
over sampled
correct sampling
under sampled
“Correct” image size? 64x64, 512x512, 2048x2048, …
Nyquist – Shannon sampling theory: Proper spatial sampling
2.3 – 3 times smaller than optical resolution (x, y, AND z)
Adjust zoom, binning, and image size (no of pixels)

## Slide 17: Nyquist sampling criterion
General form
Digital sampling frequency > analogue frequency x 2
Spatial representation
Image pixel size x 2.3 = smallest resolvable distance
Microscopy
Image pixel size x 2.3 = optical resolution (d)

## Slide 18: Aliasing problems...
Pixel size relative to projected image
Image of object varies, depending on where it falls on detector
-
Especially for small objects close to pixel size

## Slide 19: Pixel size / Spatial Calibration
Pixel size is determined by the microscope system!
CCD photodiode “pixel” size - Magnification X
  Point scanner settings – zoom and image size
    Field of View Size - No. of Samples or “pixels”
It might be changed / lost during processing
It is stored in the “Meta Data”

## Slide 20: Pixel Size / Spatial Calibration
?
0.9 µm
?
?
?
?

## Slide 21: The digital image: Bit Depth
Photons induce transport of electrons.
Transport of electrons generates voltage.
Generated voltage is proportional to number of incoming photons.

## Slide 22: “Intensity” Digitisation
Bit Depth
Measured intensity by detector
“Bucket” holds
0-9 electrons
5 electrons counted
Corresponding level in image
Bit depth: 10 (0 to 9)levels
Level 5 selected for
RAW data “image”
digitization

## Slide 23: “Intensity” Digitisation
“digital“ intensity
resolution: 10
“digital“ intensity resolution: 20
“real” analogue intensities
9
0
19
0
Bit Depth

## Slide 25
Brief explanation of digital imaging
Binary | Hex | Decimal | Color
00000000 | 00 | 0 | Black
11111111 | FF | 255 | White
10111001 | B9 | 185 | Gray
Black, white, 254 shades of gray
Color-table dependent!
Gray LUT
Green LUT
Thermal LUT
5 ramps LUT

## Slide 26: “original” - linear blue
Grayscale - linear
altered brightness/contrast | 
data changed/lost! | 
Rainbow lookup table |  | 
better see and also compare different |  | 
intensity levels |  | 

## Slide 27: The histogram

## Slide 28: Intensity / Exposure / Saturation

## Slide 29: Intensity / Exposure / Saturation
x
pixel intensity
0
255
Bye Bye Data!
clipped
overexposed saturated
in range
Do NOT over expose / saturate your image!!!
Why not?  Lost Information!
Use “Look Up Tables (LUT) / palettes to check the saturation

## Slide 30: Image Intensity Histograms - Use them!
intensity
0
255
log no. of pixels
OK!
Lost Info! Clipped!
255
0
255
?
0 30
In Histograms: easily see problems for image quantification!
30 = 0 ???!!!

## Slide 31: Intensity Histogram
OK
not OK - why?
Fluorescence Microscopy

## Slide 32: Intensity Histogram

## Slide 33: Line Profile
FWHM
FWHM= “Full Width at Half Maximum”
for measurements
50% of
max. intensity
0.9 µm

## Slide 34: Image quality

## Slide 36: Image plus meta data

## Slide 37: ImageJ using FIJI

## Slide 38: What is Fiji and ImageJ
Open source https://imagej.net/downloads
Advantages and disadvantages
  Free
  Fairly easy to use
  Programmable
  Thousands of all ready developed ‘plugins’
  Google probably know what you are looking for.
  Poorly documented
  Work/click intensive
  The different plugins can be very inconsistent
Currently, if one works with microscopy, ImageJ is unavoidable!

## Slide 39
File - Open Samples - Embryos
Spatial Scaling:
Can you measure the length and area of objects?
 See Fiji Tutorial - SpatialCalibration (search Wiki)
Analyze - Set Scale, Analyze-Tools-Scale Bar
Line and ROI selection - ctrl M (cmd M)
Rectangle, Oval, Polygon, Freehand, Angle, Point, Wand.
Analyze - Set Measurements (Results – Edit - summarize)

## Slide 40
File - Open Samples - Neuron
Intensity clipping/ saturation and offset:
Bit Depth – change from 16 to 8. What happens to the numbers?
Brightness/Contrast: Image-Adjust-Brightness/Contrast. Realize: you can loose data using “Apply”!
Intensity Histograms: log scale for fluorescence

## Slide 42: RGB Color Space
19
0
R G B
Why RGB? ... because we have red, green and blue sensitive photo receptors in our eyes!
Each “colour” is really just single greyscale numbers!

## Slide 43: Scatterplot / 2D Histogram/ Colocalization Analysis
R shifted +20 pix
R shifted +10 pix
original R+G
Find a way to visualise what you actually want to see:
Here, we don’t care WHERE the beads are; We care if they are in the same place or not!
Red intensity
Red intensity
Red intensity
Green intensity
Green intensity
Green intensity

## Slide 44: Pearson’s Image Correlation Coefficient (Manders et al., 1993)
Correlation between images, r ranges from -1 to +1
+1 means full correlation (images are the same) 0 means no correlation (random)
-1 means full anti correlation (no red where there is green)

## Slide 45: Pearson’s Image Correlation Coefficient
r = +1
r = -1
r = 0
r > 0
In English…per pixel and summed for the whole image:

## Slide 46: Pearson’s Image Correlation Coefficient is…
Insensitive to diff. intensity of the 2 images. Insensitive to intensity offset.
If red is 1/2 as bright as green…
Still can get r = 1
… so Pearsons r is is robust for biological imaging…

## Slide 47
File - Open Samples - Neuron
RGB colour space:
Colour channels – Image-Colour-Channels Tool, Split channels etc.
LookUp Tables/Paletts: Image - Lookup tables, or LUT toolbar icon
Histogramm: Analyze-Histogram
Intensity Scale: Analyze – Tools - Calibration bar
Getting to know “Fiji” better – Fiji is just ImageJ http://pacific.mpi-cbg.de

## Slide 48: Working with multi dimensional images
More than one frame, time point or channel
Ortho view, montage and other ways of looking at >2D image
3D volume
File - Open Samples - confocal-series.tif
Make a montage: Stk Make montage

## Slide 49: Image processing masks and filters
Introduction
  Neighbourhood
  Operation on neighbourhood
Spatial filters
  Mean and Median filter
  Edge detection

## Slide 50: A. Introduction
Neighbourhood (or kernel): pixels that matter
“Transformation or set of transformations where a new image is obtained by neighbourhood operations.”
The Intensity of a pixel in the new image depends on the intensity values of “neighbour pixels”

## Slide 51
3 x 3

## Slide 52
5 x 5

## Slide 53: B: Filtering - the mean filter
Simplest filter: The value of a pixel is replaced by the intensity mean of the neighbourhood pixels.
3x3 example:

## Slide 54: The mean filter
“The new pixel value depends on a linear combination of neighbourhood pixel values”
(The order of several linear filters in sequence does not matter)
The mean filter is a linear filter!

## Slide 56: The mean filter
blurs images - small details are lost (low pass filter)
smoothes edges dramatically
fails for salt & pepper noise
Main property: low-pass filter (smooths small objects)
kernel size influence
number of successive applications
+ simplest filter – fast
+ it’s a linear filter
+ averages noise, does not eliminate it
+ works against Gaussian and Poisson noise

## Slide 57: Linear filtering - Properties
Applying a linear filter to an image is the same as: applying it to all parts, then summing the results.
When applying a succession of linear filters: the order filters are applied in does not matter.
Mathematical framework underlying it: Convolution.
We can also reverse the process : Deconvolution

## Slide 58: The Gaussian filter
smooths Poisson noise
linear Filter
makes more mathematical sense than mean filter?
...properly spatially sampled image, looks like PSF
can vary the sigma value: number of pixels
varying degree of blur.
Gaussian Curve - Bell Shaped function

## Slide 59: The median filter
The value of a pixel is replaced by the median of the pixel intensity in neighbour pixels
5 112 86
235 88 211
137 233 108
Take neighbourhood (e.g. 3x3)
Sort it
5
86
88
108
112
137
211
233
235
Take median
112

## Slide 60: The median filter
5 | 9 | 6 | 6 | 9 | 5 | 9
9 | 5 | 9 | 7 | 8 | 7 | 9
8 | 9 | 8 | 6 | 7 | 9 | 9
9 | 9 | 7 | 200 | 9 | 6 | 9
6 | 5 | 8 | 6 | 9 | 6 | 7
9 | 7 | 9 | 9 | 8 | 6 | 7
7 | 9 | 5 | 6 | 7 | 6 | 6
outlier
0 | 5 | 6 | 6 | 6 | 7 | 0
5 | 8 | 7 | 7 | 7 | 9 | 7
8 | 9 | 8 | 8 | 7 | 9 | 7
6 | 8 | 8 | 8 | 7 | 9 | 6
6 | 8 | 8 | 9 | 8 | 7 | 6
6 | 7 | 7 | 8 | 6 | 7 | 6
0 | 7 | 6 | 6 | 6 | 6 | 0
Median filtered:
Original:
The outlier value has been completely removed from the dataset
noise elimination

## Slide 61: The median filter
-Slower than mean (not such a problem anymore... computers are fast)
- NOT linear
+ Typically good for “Salt & pepper” noise removal
+ Eliminates noise
+ Edge-preserving

## Slide 64
File - Open Samples – Neuron
Convolve a simple binary image
  Process – Filters – Convolve (play with different kernels)
(2) Noisy sample image
Mean and Median Filter (change pixel number, kernel size)
Simple Image Filtering

## Slide 65: What is “Image Segmentation”?
“Greyscale” image
Foreground background

## Slide 66: What is “Image Segmentation”?
“Scalar Intensity” image
“Binary” image

## Slide 67: What is “Image Segmentation”?
“Scalar Intensity” image
“Binary” image
1 | 65 | 13 | 55 | 2
2 | 3 | 34 | 2 | 1
4 | 0 | 31 | 1 | 2
1 | 33 | 3 | 54 | 3
56 | 3 | 2 | 1 | 34
0 | 1 | 1 | 1 | 0
0 | 0 | 1 | 0 | 0
0 | 0 | 1 | 0 | 0
0 | 1 | 0 | 1 | 0
1 | 0 | 0 | 0 | 1

## Slide 68: What is “Image Segmentation”?
“Scalar Intensity” image
Labeled objects

## Slide 69: What is “Image Segmentation”?
High Information Content 65536 pixels, 0-255 value
Lower Information Content, but easier to interpret
biological meaning…
45 “objects” with properties: size, shape, intensity etc.

## Slide 70: “Thresholding” (Intensity Histogram Split)
Clear difference between foreground and background?
Image not very noisy?
Choose an intermediate grey value = “threshold”
Determines foreground and background.

## Slide 71: “Thresholding” (Intensity Histogram Split)
How to choose the grey level for thresholding?
Look at pixel intensity histogram of whole image…
Is there an obvious place?

## Slide 72: “Thresholding” (Intensity Histogram Split)
“Greyscale” image
Create foreground background using: auto threshold  otsu

## Slide 73: Computed Global Threshold Objective - Reproducible
Initial guess of Threshold, T
Compute mean pixel intensity of
background and foreground
Tnew = 0.5 x (mean of foregrnd
+ mean of bkgrnd)
Iterate until Tnew no longer
changes.
Note:
Manual threshold set?
Make Binary uses that dumb threshold!
ImageJ - Image - Adjust - Threshold - Auto (=Make Binary):

## Slide 74: Practical Session 2c
File - Open Samples – Blobs (inverse)
Thesholds
  Image - Adjust - Auto Threshold and Auto Local Threshold
  Many more methods, and “local” method
Simple Image Segmentation

## Slide 75: Deconvolution

## Slide 76: Image formation – convolution of signal
Object
Confocal PSF
x
Acquired image
Convolution + noise
Notes: Widefield

## Slide 77: Deconvolution
Object
Confocal PSF
x
Acquired image
Convolution + noise
?
Notes: Widefield

## Slide 78: ConvolutionDeconvolution
Point Spread Function (PSF)
Restore object based on knowledge about PSF

## Slide 79
Deconvolution of WF image
Deconvolution reveals structure hidden caused by imaging acquisition

## Slide 80: Topics:
ImageJ / FIJI
Basic properties of digital images (sampling, formats, size, depth, )
Image enhancement (how to make your image look better)
  histograms, LUT, contrast enhancement
  background subtraction
  filter masks (smoothing and sharpening)
Working with image stacks
Colocalization
Image segmentation by thresholding
Deconvolution